## Slide 1: External Events
Sometimes, external events occur and these issues are relevant:
When the event might occur can’t be predicted beforehand.
Because the event is only valid for a short period of time, it must be responded to quickly.
If the event isn’t handled promptly, the next occurrence of the event will destroy information related to the current event.
The main program running on the CPU has no code to handle the event and the main program source code isn’t available to add code to handle the event.

## Slide 2: 6502 Interrupts (IRQ)
There’s a special IRQ (Interrupt Request) line going into the 6502 CPU. If the line is HIGH, program operation proceeds normally. If the line is pulled LOW, the currently executing instruction finishes (which can take as long as 6 clock cycles) and then, before the next opcode is fetched, the following “interrupt sequence” is initiated:

## Slide 3: IRQ Service Routine
If IRQ interrupts are enabled (i.e., allowed to occur), then the hardware generated “subroutine call” sequence will store the program counter and processor status at the time of the interrupt on the stack and set the program counter to the first instruction of your ISR (Interrupt Service Routine). This address is stored in the two bytes (low order first, then high order) at the special address $FFFE and $FFFF.
Your ISR does whatever is necessary to respond to the IRQ and then executes an RTI (Return from Interrupt) instruction. This will restore the processor status and program counter from the stack and main program execution will resume exactly where it was interrupted.